KILLER TOOLS & Equipment Corporation

6105 Main Ave., Suite 11, Orangevale, Ca., 956622

800-369-4262

INSTRUCTIONS FOR OPERATING ART38 DENT REMOVAL EQUIPMENT

DENT PULLING:

- The Killer Tools website and databases are all intended to be used as a GUIDE ONLY - it is important to remember that the auto body professional performing the repair is able to thoroughly inspect, diagnose and identify the methodology of the repair and will make that determination.

- Always wear safety Glasses and gloves while using this equipment

- Do not use outdoors or around water as this could be hazardous and could afflict bodily injury or death,

- Attach electrode to handle

- Plug machine into appropriate outlet for machine (110v or 220v)

- Turn timer switch to lowest number (1) Increase to 2 if needed

- Place ground magnet on bare metal as close to work area as possible

- Lightly hold electrode to area of damage (Clean bare metal)

- Pull trigger to create weld, and then pull firmly and straight until dent has been removed

- Twist handle to break weld and repeat.

WELDING WIGGLE WIRE:

- Turn timer to 3.

- With one hand, hold wiggle wire onto area to be repaired

- Place copper shrinking tip on handle into wiggle wire and press trigger

- Use pulling claw to grasp wiggle wire and pull with appropriate pulling tool

NOTE: The higher the timer, the more heat generated and the harder it will be to remove wiggle wire