KILLER TOOLS & Equipment Corporation

ART38-SC assembly

- Remove contents of carton.

- Install casters through square hole in black base/tray and fasten with barrel nut and 5mm hex key.

- Install right and left upright brackets using 4 60mm bolts with 1 washer, and 1 nut each bolt using a 14mm wrench.

- Install seat using 4 Phillips screws.

- Install yellow pull handle brackets so that pull handle angles away from seat using 4 60mm bolts, 4 washers, 4 nuts.

- Install black 150mm connecting tubes to “U” shaped pull handle using 2 34mm bolts, 2 washers, 2 nuts.

- Install 2 black “Z” brackets to “U” shaped pull handle using 2 20mm bolts and 2 washers.

- Install “u” shaped pull handle into pull handle brackets so that the “Z” brackets face the seat, for proper weight distribution.

- Make sure all fasteners are sufficiently tightened.

- Install Killer Tools 38 series steel electrode dent puller into tray under seat, and you are ready to use.

**WARNING**

DO NOT LEAN ON OR USE PULL HANDLE AS BACK REST. This can cause the cart to tip over causing great bodily harm.

# Text boxes

6105 Main Ave. Suite 11, Orangevale, Ca., 95662

Phone: 800-369-4262  Fax 800-810-4513